## Slide 1: ROS - Lesson 1
Teaching Assistant: Roi Yehoshua
roiyeho@gmail.com

## Slide 2: Agenda
Introduction to ROS
ROS Main Features
ROS Main Concepts
Basic ROS Commands
Turtlesim Demo

## Slide 3: The Problem
Lack of standards for robotics

## Slide 4: What is ROS?
ROS is an open-source robot operating system
The primary goal of ROS is to support code reuse in robotics research and development
ROS was originally developed in 2007 at the Stanford Artificial Intelligence Laboratory
Development continues primarily at Willow Garage, a robotics research institute/incubator

## Slide 5: ROS Main Features
Taken from Sachin Chitta and Radu Rusu (Willow Garage)

## Slide 6: ROS Main Features
Hardware and network abstraction
Low-level device control
Message-passing between processes
Implementation of commonly-used functionality
Package management

## Slide 7: Robots using ROS
http://wiki.ros.org/Robots

## Slide 8: ROS Philosophies
Modularity & Peer-to-peer
Language Independent
Thin
Free & Open-Source

## Slide 9: Modularity & Peer-To-Peer
ROS consists of a number of processes
  potentially on a number of different hosts,
  connected at runtime in a peer-to-peer topology
No central server

## Slide 10: Language Independent
Client interfaces:
  Stable: roscpp, rospy, roslisp
  Experimental: rosjava, roscs
  Contributed: rosserial, roshask, ipc-bridge (MATLAB), etc...
Common message-passing layer
  Interface Definition Language (IDL)

## Slide 11: Thin
Library-style development
  all development occurs in standalone libraries with minimal dependencies on ROS
ROS re-uses code from numerous other open-source projects, such as the navigation system simulators and vision algorithms from OpenCV

## Slide 12: Free & Open-Source
Source code is publicly available
Contributed tools are under a variety of open-source (& closed-source) licenses
Promotes code-reuse and community-building

## Slide 13: ROS Core Concepts
Nodes
Messages and Topics
Services
ROS Master
Parameters

## Slide 14: ROS Nodes
Single-purposed executable programs
  e.g. sensor driver(s), actuator driver(s), mapper, planner, UI, etc.
Modular design
  Individually compiled, executed, and managed
Nodes are written with the use of a ROS client library
Nodelets

## Slide 15: ROS Client Libraries
A collection of code that eases the job of the ROS programmer.
Libraries that let you write ROS nodes, publish and subscribe to topics, write and call services, and use the Parameter Server.
Main clients:
  roscpp = C++ client library
  rospy = python client library

## Slide 16: ROS Topics
Nodes communicate with each other by publishing messages to topics
Publish/Subscribe model: 1-to-N broadcasting
Examples:
  provide sensor readings
  provide actuator states / robot feedback

## Slide 17: More Complex Example

## Slide 18: ROS Messages
Strictly-typed data structures for inter-node communication
Messages can include:
  Primitive types (integer, floating point, boolean, etc.)
  Arrays of primitives
  Arbitrarily nested structures and arrays (much like C structs)
For example, geometry_msgs/Twist.msg
Vector3 linear
Vector3 angular

## Slide 19: ROS Services
Synchronous inter-node transactions / RPC
Service/Client model: 1-to-1 request-response
Service roles:
  carry out remote computation
  trigger functionality / behavior
For example, the explore package provides a service called explore_map which allows an external user to ask for the current map

## Slide 20: ROS Master
The role of the master is to enable ROS nodes to locate one another
Naming & registration services for nodes, topics, services, etc
Run using the roscore command

## Slide 21: Parameter Server
A shared, multi-variate dictionary that is accessible via network APIs.
Best used for static, non-binary data such as configuration parameters.
Runs inside the ROS master

## Slide 22: ROS Packages
Software in ROS is organized in packages.
A package contains one or more nodes and provides a ROS interface

## Slide 23: Package Examples
explore - frontier-based exploration.
move base - implements the action of movement to a destination location
gmapping - provides laser-based SLAM (Simultaneous Localization and Mapping) using a grid map.
stageros - implements two-dimensional robot simulation using Stage.

## Slide 24: ROS Package System
Taken from Sachin Chitta and Radu Rusu (Willow Garage)

## Slide 25: ROS Package Repositories
Collection of packages and stacks
Many repositories (>50): Stanford, CMU, Leuven, USC, …
Most of them hosted in GitHub
http://wiki.ros.org/RecommendedRepositoryUsage/CommonGitHubOrganizations

## Slide 26: ROS Hydro
Latest ROS version is ROS Hydro Medusa
ROS Hydro Medusa is the 7th ROS distribution
Released on September 4th 2013
Moved to a new packaging system called catkin

## Slide 27: ROS Supported Platforms
ROS is currently supported only on Ubuntu
  other variants such as Windows and Mac OS X are considered experimental
ROS distribution supported is limited to <=3 latest Ubuntu versions
ROS Hydro supported on:
  Ubuntu Precise (12.04 LTS)
  Ubuntu Quantal (12.10)
  Ubuntu Raring (13.04)

## Slide 28: ROS Installation
Follow the instructions at:
  http://wiki.ros.org/hydro/Installation/Ubuntu
  Easy installation, takes about 20 mins
  Note: Installation takes 2,442MB space of your HD
To test your installation, follow the ROS tutorials:
  http://wiki.ros.org/ROS/Tutorials

## Slide 29: ROS Installation

## Slide 30: Setting Up ROS Environment
Add the following line to your bash startup file (typically ~/.bashrc):
  source /opt/ros/hydro/setup.bash

## Slide 31: Basic ROS Commands
roscore – a collection of nodes and programs that are pre-requisites of a ROS-based system
roscore is defined as:
  master
  parameter server
  rosout
Usage:
  $roscore

## Slide 32: Basic ROS Commands
rosrun – allows you to run an executable in an arbitrary package without having to cd (or roscd) there first
Usage:
  $rosrun package executable
Example
  Run turtlesim
    $rosrun turtlesim turtlesim_node

## Slide 33: Basic ROS Commands
rosnode – Displays debugging information about ROS nodes, including publications, subscriptions and connections
Commands:
 | Command
List active nodes | $rosnode list
Test connectivity to node | $rosnode ping
Print information about a node | $rosnode info
Kill a running node | $rosnode kill
List nodes running on a particular machine | $rosnode machine

## Slide 34: Demo - Turtlesim
In separate terminal windows run:
  roscore
  rosrun turtlesim turtlesim_node
  rosrun turtlesim turtle_teleop_key

## Slide 35: Demo - Turtlesim

## Slide 36: ROS Simulators
Stage - 2D Simulator
Gazebo - 3D Simulator
In this course we will use Stage

## Slide 37: Stage Simulator

## Slide 38: More Information about ROS
ROS Cheat Sheet
  http://u.cs.biu.ac.il/~veredm/89-689/ROScheatsheet.pdf
ROS Tutorial Videos
  http://www.youtube.com/playlist?list=PLDC89965A56E6A8D6

## Slide 39: Homework (not for submission)
Install ROS
Read and perform all the Beginner Level tutorials
  http://wiki.ros.org/ROS/Tutorials