## Slide 1: Multi-Robot Systems with ROS Lesson 1
Teaching Assistant: Roi Yehoshua
roiyeho@gmail.com

## Slide 2: Course Agenda
Working with multi robots in ROS
Handling communication and synchronization between robots
Canonical multi-robot problems in ROS
  Patrolling, Formation, Coverage, etc.
Decision making system
  We will be using CogniTAO, a decision making system developed by Cogniteam

## Slide 3: Course Requirements
Course grade will be composed of:
  40% Assignments
  40% Project
  20% Exam

## Slide 4: Who am I?
My name is Roi Yehoshua
PhD Student at Bar-Ilan Robotics lab headed by Prof. Gal Kaminka
Teaching assistant at the courses:
  Introduction to Robotics (89-685)
  Multi-Robot Systems (89-689)
My home page: http://u.cs.biu.ac.il/~yehoshr1/

## Slide 5: Today’s Agenda
ROS Recap
Turtlesim Demo
Intro to Multi-Robots Systems in ROS

## Slide 6: What is ROS?
ROS is an open-source robot operating system
The primary goal of ROS is to support code reuse in robotics research and development
ROS was originally developed in 2007 at the Stanford Artificial Intelligence Laboratory and development continued at Willow Garage
Today managed by the Open Source Robotics Foundation
ROS Wiki

## Slide 7: ROS Main Features
ROS has two basic "sides"
The operating system side, which provides standard opearting system services such as:
  hardware abstraction
  low-level device control
  implementation of commonly used functionality
  message-passing between processes
  package management
A suite of user contributed packages (organized into sets called stacks) that implement common robot functionality such as SLAM, planning, perception, simulation etc.

## Slide 8: ROS Distributed Architecture

## Slide 9: ROS Core Concepts
Nodes
Messages and Topics
Services
ROS Master
Parameters
Stacks and packages

## Slide 10: ROS Nodes
Single-purposed executable programs
  e.g. sensor driver(s), actuator driver(s), mapper, planner, UI, etc.
Modular design
  Individually compiled, executed, and managed
Nodes are written using a ROS client library
  roscpp – C++ client library
  rospy – python client library
Nodes can publish or subscribe to a Topic
Nodes can also provide or use a Service

## Slide 11: ROS Topics
Nodes communicate with each other by publishing messages to topics
Publish/Subscribe model: 1-to-N broadcasting

## Slide 12: ROS Topics
A shared topic can be used to send messages between different robots

## Slide 13: ROS Messages
Strictly-typed data structures for inter-node communication
For example, geometry_msgs/Twist is used to express velocity broken into linear and angular parts:
Vector3 is another message type composed of:
Vector3 linear
Vector3 angular
float64 x
float64 y
float64 z

## Slide 14: ROS Services
Synchronous inter-node transactions / RPC
Service/Client model: 1-to-1 request-response
Service roles:
  carry out remote computation
  trigger functionality / behavior
Example:
  map_server/static_map – retrieves the current occupancy grid map

## Slide 15: ROS Master
Enable ROS nodes to locate one another
Think of it as a ROS directory service, sort of DNS
  Provides naming & registration services for nodes, topics, services, etc

## Slide 16: Parameter Server
A shared, multi-variate dictionary that is accessible via network APIs.
Best used for static, non-binary data such as configuration parameters.
Runs inside the ROS master

## Slide 17: ROS Packages
Software in ROS is organized in packages.
A package contains one or more nodes and provides a ROS interface

## Slide 18: ROS Package System
Taken from Sachin Chitta and Radu Rusu (Willow Garage)

## Slide 19: ROS Important Packages
 | Package
Maintains the relationship between multiple coordinate frames over time | TF
Provides a standardized interface for interfacing with preemptable tasks. | actionlib
Provides laser-based SLAM (Simultaneous Localization and Mapping) using a grid map | gmapping
a probabilistic localization system for a robot moving in 2D | amcl
Print information about a node | move_base
Stage 2-D multi-robot simulator | stage_ros

## Slide 20: ROS Command-Line Tools
rostopic (Topics)
rosservice (Services)
rosnode (Nodes)
rosparam (Parameters)
rosmsg (Messages)
rossrv (Services)
roswtf (General debugging)

## Slide 21: ROS Visualization Tools
rqt – ROS integrated graphical user interface
rviz – 3D visualization tool for ROS

## Slide 22: Installing ROS
Make sure you have a recent Linux Ubuntu installation (12.04 and above)
  64bit installation is recommended
Latest version of ROS is called Hydro (released on September 2013)
Follow the installation instructions in http://wiki.ros.org/hydro/Installation/Ubuntu

## Slide 23: Install Terminator
Terminator is a program that allows you to manage multiple terminals in one window and use key bindings to switch between them.
To install terminator type:
To run terminator for the first time type:
By right clicking on the terminator window you can choose to split it horizontally/vertically
  $ sudo apt-get install terminator
  $ terminator

## Slide 24: Terminator

## Slide 25: roscore
roscore is the first thing you should run when using ROS
roscore will start up:
  a ROS Master
  a ROS Parameter Server
  a rosout logging node
  $ roscore

## Slide 26: rosrun
rosrun allows you to use the package name to directly run a node within a package
Usage:
Example:
  $ rosrun <package> <executable>
  $ rosrun turtlesim turtlesim_node

## Slide 27: TurtleSim Demo
Now we will try to run two turtlesim nodes at the same time
First start the ROS infrastructure by running in a terminal the command:
Then start the first turtle simulator node by running in a new terminal:
  $ roscore
  $ rosrun turtlesim turtlesim_node

## Slide 28: TurtleSim Demo

## Slide 29: ROS Topics
To display the list of current topics, use the following command:
  $ rostopic list

## Slide 30: Publish to ROS Topic
Use the rostopic pub command to publish messages to a topic
For example, to make the turtle move forward at a 0.2m/s speed, you can publish a cmd_vel message to the topic /turtle1/cmd_vel:
You can specify only the linear x velocity:
  $ rostopic pub /turtle1/cmd_vel geometry_msgs/Twist '{linear: {x: 0.2, y: 0, z: 0}, angular: {x: 0, y: 0, z: 0}}'
  $ rostopic pub /turtle1/cmd_vel geometry_msgs/Twist '{linear: {x: 0.2}}'

## Slide 31: Publish to ROS Topic
Some of the messages like cmd_vel have a predefined timeout
If you want to publish a message continously use the argument -r with the loop rate in Hz (default is 10Hz)
For example, to make the turtle turn in circles: continuously
  $ rostopic pub /turtle1/cmd_vel -r 10 geometry_msgs/Twist '{linear: {x: 0.2, y: 0, z: 0}, angular: {x: 0, y: 0, z: 0.5}}'

## Slide 32: Publish to ROS Topic

## Slide 33: rqt
rqt provides the main to start an instance of the ROS integrated graphical user
rqt contains many plugins that can help you perform various operations in ROS
  List of plugins
To start rqt type the following command:
  $ rqt

## Slide 34: rqt

## Slide 35: ROS Graph Plugin
Visualizes the ROS computation graph

## Slide 36: Publisher Plugin
Publishes arbitrary messages (similar functionality to rostopic pub).

## Slide 37: Intro to Multi Robot Systems in ROS
Three options to run a multi-robot system in ROS:
Running multiple instances of the same node on the same computer
Running multiple nodes on different computers using one common roscore
Establishing a multi-master network

## Slide 38: Homework (not for submission)
Make sure you have a working installation of ROS Hydro
If you are unfamiliar with ROS perform all the Beginner Level tutorials
  http://wiki.ros.org/ROS/Tutorials